## Slide 1: Multiple Target Localisation at over 100 FPS
Simon Taylor
Tom Drummond
Department of Engineering
University of Cambridge, UK
This work was supported by The Boeing Company

## Slide 2: Problem: Fast Localisation
Known Target
Camera Image
Localised Target

## Slide 3: Local Feature Methods
Interest Region Detection
Region Matching
Descriptors
Classifiers
SIFT
MOPS
GLOH
Randomised Trees
Ferns
Notes:   Factor out common image transformations (translation, rotation, scale, affine...)
  Match query regions to database ones
  ...despite appearance differences which remain after region detection

## Slide 4: Quantised Patches
Sparsely sampled 8 x 8 rectangular patch
Quantised relative to μ and σ of samples
Original Image Patch
Sparse Sampling
Quantised
Image Patch

## Slide 5: Training Set
Artificially warped views of entire target from different viewpoints
Grouped into “viewpoint bins”
Scale Bin 4
Viewpoint Centre
“Reference Frame”
Warped Views
Scale Bin 8
Viewpoint Centre
Warped Views

## Slide 6: Extracting Subfeatures
FAST-9 Interest Points
Orientation Estimation→
Rotate Sampling Grid
Bilinear Sampling
Quantisation
Notes: Show interest points detected in 3 images (r, g, b)
Show one with the quantised patch

## Slide 7: Clustering Subfeatures
Known warp
Select most
repeatable
Notes: Warp previous images into reference frame
Show 2 demo clusters

## Slide 8: Histogrammed Intensity Patches
Histogram of intensity for each sample
... 1081 subfeatures in total

## Slide 9: Binary Representation
Histogram values quantised to 1-bit
40 bytes per feature model
00001 00001 11000 11110

## Slide 10: Dissimilarity Score
Count of pixels in “rare” bins for a feature
00001 00001 11000 11110
Matching Patch
00010 00010 00001 00001 … - Patch
00001 00001 11000 11110 … - HIP
00000 00000 00000 00000 … - ANDed
Bitcount(ANDed) = 0+
Non-matching Patch
10000 10000 10000 10000 … - Patch
00001 00001 11000 11110 … - HIP
00000 00000 10000 10000 … - ANDed
Bitcount(ANDed) = 2+

## Slide 11: Binary Tree Lookup
Exploits similarity between HIPs to avoid exhaustive search
011010100
011010101
011010100
010100011
110010100
001100010
010010100
010100011
001100010
000100010
011010100
010100011
011010101
110010100
001100010

## Slide 12: Viewpoint Consistency
Hough transform on target ID, scale, rotation
Check vector between matches is reasonable

## Slide 13: Comparison with Wagner et al. 2008
Wagner et al. 2008 tested on 7 sequences
  Total frame time around
  5ms on average
  Around 96% of frames
  localised successfully
Ad Book Cars Map Panorama Photo Vienna

## Slide 14: Comparison with Wagner et al. 2008
Over 4x faster
More robust
Memory usage 5-10 times lower

## Slide 15: Multiple Target Localisation

## Slide 16: Multiple Target Localisation
Under 7.5ms with all 7 targets in database
Small robustness penalty from
  Additional matching targets
  Indexing

## Slide 17: Conclusions
Classification-based matching can provide robust and fast localisation
HIPs provide a memory and computationally efficient model for features
Training phase can limit the impact of fast but inaccurate region detection approaches
Tree-based lookup allows exact classification results without exhaustive comparison